Azimuths

An azimuth is the angle between the North line and a given direction represented by a direction arrow; it is measured in the clockwise direction.

The arrow shows direction, the

azimuth is taken from the endpoint

without the arrow.

Every line segment has two azimuths, depending upon the endpoint from which it is taken.

Given an azimuth:

2250                                  i) If the angle is less than 1800, then add

1800 to obtain the other azimuth.

1800 + 450 = 2250

ii) If the angle is greater than 1800, then

2250 – 1800 = 450         subtract 1800 to obtain the other

azimuth.

Example 1: For the following azimuths:

- sketch the azimuth showing the North line

- find the azimuth from the other endpoint

- sketch this azimuth showing the North line.

a) 240

Finding the Angle between Two Azimuths

It is easier to find the angle between two azimuths if they are measured from a common endpoint.

Example 1:

To determine the measure of theta, simply subtract

400 from 2100.  The measure of  is 1700. The

process for arriving at this result is shown below.

Step 1:

It is easier to determine the angle between the two azimuths

if the diagram is sketched to represent the measurement of

both azimuths from a common endpoint.

Step 2:

Now subtract the angles:

Example 2:  Determine the measure of  in the following diagram:

1500

θ

2800

Solution 2:

same point

1800 + 1500 = 3300                              2800 – 1800 = 1000

So:

Exercises:

1. For the azimuth of 3550:

- sketch the azimuth showing the North line

- find the azimuth from the other endpoint

- sketch this azimuth showing the North line.

2. Find θ in the following diagram:

Solutions:

1.

3550 – 1800 = 1750

- 850 + 1800 = 2650

2650 – 300 = 2350

# Text boxes

N

225°

N

45°

N

450

N

b) 1850

210°

θ

220°

210°

θ

40°